## Slide 1: DTC and General Information Screen
Displays TCM/VCM information including:
  Active and inactive DTCs.
  System ID.
  TCM ignition voltage.
  Oil level.
  Sump oil temperature.
  ESS temperature.
  ESS SPN/FMI information.
  CAN Error Frame information.
Notes: <number>

## Slide 2: Graphical View
Displays diagnostic data using gauges, thermometers and indicator lights including:
  Engine speed.
  Service brake applied status.
  Drive unit output shaft speed.
  Motor temperatures.
  Drive unit fluid temperature.
  ESS temperature.
  ESS DC voltage level.
  TCM voltage.
  Input/Output wire states.
Notes: <number>

## Slide 3: Data Monitor
Presents a real-time look at what is occurring in the H 40/50 EP System.
Diagnostic information is grouped by category in the left pane.
Input/Output wire information is listed in the right pane.
  Pushbutton Shift Selector (PBSS) category is only displayed when connected to systems equipped with Allison 4th Generation Controls.
  Pushbutton Shift Selector (PBSS) category is only displayed when connected to systems equipped with Allison 4th Generation Controls.
Notes: <number>

## Slide 4: ESS Data Monitor
Expand a category in the right pane using the plus sign.
Select the data category to be requested from the ESS.
  A green light illuminates indicating the category is selected.
  Real-time data is transmitted from the ESS via the J1939 datalink.
Closing the Request ESS Data window terminates all information requests from the ESS.
Notes: <number>

## Slide 5: Custom Data Monitor
Allows technicians to choose the data points to display in the Data Monitor window.
  Specific data can be selected for a more focused view of diagnostic information.
  Data list configurations can be saved and recalled for later use.
Even though de-selected data is not displayed, it is still being requested by the Allison DOC® software.
  ESS data must be requested via the Request ESS Data window before it will be displayed in the Custom Data Monitor.
Notes: <number>

## Slide 6: Calibration Information
Displays current calibration information including:
  Customer Modifiable Constants.
  SID (System Identification Number).
  TCM/VCM type.
  ESS and DPIM version information.
  Input/Output wire states.
  ESS System ID information.
    BCIM year.
    BCIM revision level.
    BCIM software level.
Notes: <number>

## Slide 7: Clutch Tests
Used to check clutch pressures:
  Select a clutch to apply via the clutch tests popup window.
  Range selection and clutch information can be viewed in the Data Monitor window during the test.
  Be sure engine is running and drive unit is in Neutral before beginning a Clutch Test.
Notes: <number>

## Slide 8: Output Tests
Used to check output wiring circuits connected to the TCM/VCM.
  Current state of circuit is displayed below the selected output.
  On and Off buttons energize and de-energize selected circuit.
    Circuit on/off state is displayed in real-time.
Notes: <number>

## Slide 9: Reset Adaptives
Reset Adaptives window displays tabs containing each set of adaptive values.
  Reset Adaptives tab allows selection of adaptives to be reset.
  Clutch 1 and Clutch 2 tabs display currently stored adaptive values.
Allows learned adaptive parameters to be reset to factory defaults.
  Use after drive unit component overhaul or internal repair.
  Resetting individual range shifts aids in troubleshooting shift performance complaints.
Notes: <number>

## Slide 10: Motor Spin Tests
Allows technicians to verify the motors spin when commanded and in the direction commanded.
Select Motor A or Motor B for testing.
  Popup window allows selected motor to be spun clockwise or counter-clockwise:
Use the Data Monitor to view the rpm values for each motor during the test.
  Values will read negative during a counter-clockwise test.
Notes: <number>

## Slide 11: Reprogramming
Accessed from the Reprogram pull down.
Reprogram window displays current CMC values.
  Current values can be saved for later retrieval.
Click on a CMC value to be changed.
  Enter new value and hit enter.
Click the Reprogram System button.
  Commits changes to the TCM/VCM.
  Reprogramming is only available to technicians who pass additional training and receive a certificate enabling Reprogramming access.
Notes: <number>