## Slide 1: Introduction
Shift quality complaints range from consistent to intermittent
  Consistent complaints are easily verified
  Very intermittent complaints can be completely subjective in nature

## Slide 2: Troubleshooting Considerations
Understand the following shift behavior(s) from the customer
  Harsh
    Produces a momentary deceleration of the vehicle with enough force to jerk/shake the operator
      Result of a clutch pack applying too quickly
  Slipping
    Applied clutch does not transfer all torque input from engine to output shaft
  Delayed
    Shift does not occur in the expected time frame

## Slide 3: Troubleshooting Considerations
Understand the following shift behavior(s) from the customer (cont’d)
  Shift occurs too quickly
  Erratic
    Shift does not occur at the same vehicle speed under the same specific operating conditions
      Closed throttle/full throttle
  Flare
    Increased engine speed during shift
      Result of clutch pack applying too slowly
  Shudder
    Rapid vehicle accelerations and decelerations occurring in sequence.

## Slide 4: Troubleshooting Considerations
Which shifts are affected?
Under what conditions does the shift behavior occur?
  Full throttle
  Closed throttle
  Partial throttle
  Vehicle loaded, unloaded or both
  Transmission output retarder on or off
  Engine brake on or off
  Intermittent behavior
    Define this behavior with customer
  Specific transmission temperature

## Slide 5: Troubleshooting Considerations
Attempt to reproduce customer complaint
  Verify what customer believes is occurring is in fact what the customer has described
For intermittent complaints:
  Use Allison DOC® to collect data during the test drive
    Have customer attempt to reproduce shift complaint
    Record a snapshot of the test drive session

## Slide 6: Troubleshooting Steps
Follow appropriate troubleshooting steps for any DTCs that return during test drive
  As defined by Troubleshooting Manual procedures for transmission model being diagnosed
Review Allison DOC® Failure Records
  If unable to reproduce any codes that were cleared prior to the test drive
  Review data in saved Failure Record for indication of possible causes of code generation
If DTCs and Failure Records are not present:
  Utilize the Performance Complaints feature of Allison DOC®
  Reference the Performance Complaints section of the appropriate Troubleshooting Manual

## Slide 7: Allison DOC® Failure Records
Store operating condition information at the time a DTC is logged
  Each DTC generates a Failure Record
Only updated or refreshed the first time the diagnostic test run by the TCM fails
  Occurs during each ignition cycle
Last five Failure Records can be viewed by double-clicking the “Y” under the Failure Records column of any DTC listed in the DTC & General Information screen of Allison DOC®
  Can also be accessed by clicking the Failure Records button below the DTC pane in the same screen

## Slide 8: Allison DOC® Failure Records
Replaced on a “first in, first out” basis if more than five Failure Records are stored
  DOC automatically saves the last twenty failure records as text files located on the computer hard drive in the following location:
    /Users/Public/PublicDocuments/AllisonTransmission/AllisonDOCforPC-ServiceTool/FailureRecords

## Slide 9: Possible Complaint Causes
Incorrect transmission fluid level
Shift(s) not adapted
Erratic output and/or input speed signals
Inaccurate or inoperable throttle signal
Inaccurate transmission sump temperature
Incorrectly configured ECM parameters for automatic transmissions
  Refer to Allison Technical Document #161
Clutch pressure not within specification

## Slide 10: Incorrect Fluid Level
Low level
  Insufficient quantity of fluid for proper clutch control
High level
  Causes fluid aeration
    Traps air in transmission fluid
Both conditions can cause erratic shift behavior or shift flare(s)

## Slide 11: Shifts Not Adapted
Transmission has not experienced a sufficient number of clutch applies under specific conditions when shift complaint occurs
  Example would be a 2-1 downshift at 100% throttle
Causes
  Vehicle in service for a short time
  TCM recalibration
  TCM replacement
  Adaptive Reset initiated by Allison DOC®

## Slide 12: Shifts Not Adapted
Determining if shifts are not adapted
  Connect Allison DOC® to the transmission
  Open Reports menu

## Slide 13: Shifts Not Adapted
Determining if shifts are not adapted (cont’d)
  Select Adapt Shift Reports Section
  Save report

## Slide 14: Shifts Not Adapted
Determining if shifts are not adapted (cont’d)
  Load report
    Select from drop down list
    Click Load button

## Slide 15: Shifts Not Adapted
Determining if shifts are not adapted (cont’d)
  View Report
    Look for Not Converged entries in each shift pattern
    Pattern Definitions
      Pattern 0 = Primary shift schedule
      Pattern 1 = Secondary shift schedule
      Pattern 2 = Shift made during lockup clutch apply
    Region Definitions
      Region 0 = Throttle between 0% and 50%
      Region 1 = Throttle between 50% and 80%
      Region 2 = Throttle between 80% and 100%

## Slide 16: Shifts Not Adapted
Determining if shifts are not adapted (cont’d)

## Slide 17: Speed Signals/Throttle/Intermittent Conditions
Use Snapshot feature of Allison DOC®
  Helps understand relationship between
    Throttle position
    Engine
    Turbine speed
    Output speed
DOC collects all transmission data available from the TCM
  Use Software Configuration menu to select which data points are being collected by DOC
    Only available for 4th Generation Controls and later
    Allows data to be collected at a higher rate
      Results in smoother plotting curves
      Provides more accurate speed traces

## Slide 18: Speed Signals/Throttle/Intermittent Conditions
Software Configuration setup
  Disconnect DOC from diagnostic session
  Select Software Configuration menu

## Slide 19: Speed Signals/Throttle/Intermittent Conditions
Software Configuration setup (cont’d)
  Select the appropriate Data Setup tab

## Slide 20: Speed Signals/Throttle/Intermittent Conditions
Software Configuration setup (cont’d)
  Set Frequency for the 00 identifier to Fast
    Increases sampling rate for input speed, turbine speed, output speed and throttle position
  Set Frequency for all other groups to Disabled or Slow
    Not all groups can be set to disabled
  Click Apply to save changes

## Slide 21: Speed Signals/Throttle/Intermittent Conditions
Software Configuration setup (cont’d)
  Some Dynamic Groups will not display actual parameters contained in that dynamic group
    When group is opened

## Slide 22: Speed Signals/Throttle/Intermittent Conditions
Software Configuration setup (cont’d)
  Exit Software Configuration menu and connect DOC to transmission
  Select Strip Chart function
    Configure to only plot input speed, turbine speed, output speed and throttle position
      Shows smoother curves compared to plotting all data collected from TCM at a normal rate

## Slide 23: Speed Signals/Throttle/Intermittent Conditions
Software Configuration setup (cont’d)
  Curve comparison
All data collected at normal rate
Throttle and speed data collected at highest rate with all other parameters disabled or slow

## Slide 24: Case Study #1
Issue
  Customer complaining of harsh shifts
    Vehicle mileage at complaint 79,366 (127,727 Km)
    No DTCs
Transmission
  3500 Series
Vocation
  Refuse

## Slide 25: Case Study #1
Correct fluid level verified
Snapshot shows turbine speed drop at 2:20 into file playback

## Slide 26: Case Study #1
As transmission fluid temperature increases, turbine speed becomes more erratic

## Slide 27: Case Study #1
Turbine speed sensor resistance was measured from ECU connector and found to be above specification
Turbine speed sensor resistance measured at transmission connector produced same result
Control module removed
  Inspection of internal wiring harness and turbine speed sensor connection revealed no problems

## Slide 28: Case Study #1
Turbine speed sensor resistance measured at sensor
  Measurement above specification
Replaced turbine speed sensor
  Shift complaint eliminated

## Slide 29: Case Study #2
Issue
  Customer complaining transmission will not shift from 1-2 at full throttle
  Throttle must be momentarily released to enable upshift
    Vehicle mileage at complaint 80,212 (129,089 Km)
    No DTCs
Transmission
  3500 Series
Vocation
  Dock spotter

## Slide 30: Case Study #2
Correct fluid level verified
Customer complaint duplicated on test drive
Snapshot shows turbine speed stabilizes at 100% throttle at 1898 rpm

## Slide 31: Case Study #2
Input Calibration Information Number (CIN) into PCCS and requested Shift Summary
  Determined 1-2 shift point at 100% throttle will occur at turbine speed of 1949 rpm and output speed of 559 rpm
    Reference SIL 11-TR-14 for information on Shift Summary in PCCS
Alternate method
  Select Next Upshift for Output RPM parameter in DOC Software Configuration
    Plot Strip Chart with this configuration

## Slide 32: Case Study #2
Determined engine was not producing sufficient power to accelerate above 1898 rpm at 100% throttle
  Engine inspection reveals restricted air filter
Replacing engine air filter corrects issue

## Slide 33: Case Study #3
Issue
  Customer complaining transmission locks in range intermittently
    Vehicle mileage at complaint 5,891 (9,481 Km)
    DTC P0735 & P2714
Transmission
  3000 Series
Vocation
  Delivery vehicle

## Slide 34: Case Study #3
Correct fluid level verified
DTCs recorded and cleared
Customer complaint duplicated on test drive
Snapshot shows erratic output speed during “steady state” condition

## Slide 35: Case Study #3
Output speed sensor resistance measured at TCM connector
  Reading within specification
  TCM connector securely mounted to TCM verifying output speed sensor pins are in proper position within connector
Transmission connector removed and inspected for damage and corrosion
  No issues found
Output speed sensor removed and tone wheel inspected to ensure it is not loose
  No looseness indicated when tone wheel moved radially

## Slide 36: Case Study #3
Known good output speed sensor installed in transmission and another test drive is performed
  Same issue and DTCs re-occur
Driveline physically inspected
  No mechanical issues found
Driveline angularity measured and calculated using Allison Design Calculations program
  Found to be above maximum limits

## Slide 37: Case Study #3
Excessive driveline angularity induced torsional and inertial accelerations
  Prevented tone wheel from maintaining consistent distance from tip of output speed sensor
    Caused erratic speed sensor output
    Generated DTCs

## Slide 38: Case Study #4
Issue
  Customer complaining transmission locks in range when engine temperature begins to increase
    Vehicle mileage at complaint 230,206 (370,481 Km)
    DTC 54-43 (active)
    DTC 56-33
    DTC 54-23
Transmission
  4500 Series
Vocation
  Refuse

## Slide 39: Case Study #4
Correct fluid level verified
DTCs recorded and cleared
Customer complaint duplicated on test drive and DTCs reproduced
Snapshot shows engine and turbine speed decrease idle while output speed increases
  Occurs on 3rd range preselect from 5th range

## Slide 40: Case Study #4
Only one DTC re-occurs
  Indicates incorrect speed ratio during 4-3 downshift
Both historic codes have C3 clutch in common
  Vehicle operated in ranges utilizing C3 clutch at varying throttle positions before 4:51 minutes of operation had elapsed
Pressure gauge installed in C3 and Main Pressure circuits
  Pressure measured at idle speed and 1800 rpm
  Both circuits read within specification
  Difference greater than 10 psi does not exist between C3 and Main pressure

## Slide 41: Case Study #4
Allison DOC® used to perform clutch test in 3rd range
  Turbine speed remains stationary in 3rd range at 100% throttle
Resistance measured from ECU for circuit controlling C3 clutch
  Solenoid resistance shows within specification
Control module removed
Valve body inspected
  No issues found

## Slide 42: Case Study #4
New C3 clutch solenoid installed
Road test reveals issue is resolved with new solenoid

## Slide 43: Case Study #5
Issue
  Customer complaining transmission locks in range and will not upshift
    Vehicle mileage at complaint 62,623 (100,782 Km)
    DTC 56-11 (active)
Transmission
  3000 Series
Vocation
  Dump truck

## Slide 44: Case Study #5
Correct fluid level verified
Allison DOC® connected to transmission
  Complaint reproduced on test drive
DOC shows engine and turbine speeds accelerate in first range
  Output speed does not accelerate

## Slide 45: Case Study #5
DOC used to perform clutch test
  Main, C1 and C5 pressures measured at idle
    All pressures within specification
Transmission shifted to 1st range and engine accelerated to 100% throttle
  Turbine speed remains stationary
Both tests confirm hydraulic and mechanical condition of C1 and C5 clutch packs are functioning without issue
Turbine shaft remaining stationary during clutch test indicates all planetary components are connected

## Slide 46: Case Study #5
Output speed sensor removed
Tone wheel tightness checked
  Tone wheel can be rotated while output shaft is stationary
Transmission output housing removed and disassembled
  Tone wheel found to have been battered on drive pin
    Created notch in tone wheel
    Broke drive pin allowing tone wheel to rotate independently from output shaft
Replacing affected components corrected complaint

## Slide 47: Case Study #6
Issue
  Customer complaining of 2-1 shift flare and intermittent harsh shifts
    Vehicle mileage at complaint 156,132 (251,270 Km)
    No DTCs
Transmission
  3000 Series
Vocation
  School bus (rear engine)

## Slide 48: Case Study #6
Correct fluid level verified
Harsh intermittent downshifts apparent during test drive
Snapshot reveals all speed signals become erratic upon throttle release

## Slide 49: Case Study #6
Further investigation shows that speed signals can be made to become erratic when transitioning to closed throttle in 5th range.
Curve of engine and turbine speed signals mirror output speed signal
  Indicates tone wheel is not loose
Speed signals becoming erratic at closed throttle eliminates engine issues
Driveline inspected
  Universal joint condition is acceptable
  No sign of damage

## Slide 50: Case Study #6
Rear suspension inspection reveals loose airbag mounts
  Causes axle housing to pivot excessively during “coast” condition
    Creates excessive angularity on U-joint connecting axle pinion shaft to driveline
Tightening airbag mounts corrects issue

## Slide 51: Case Study #7
Issue
  Customer states shudder will occur within two minutes of engine attaining operating temperature
    Vehicle mileage at complaint 12,854 (20,687 Km)
    No DTCs
    Cycling ignition switch when engine is at operating temperature causes shudder to occur only once within two minutes of operation time.
      Can be reproduced consistently by cycling ignition switch with engine at operating temperature
Transmission
  3060PR Series
Vocation
  Fire truck

## Slide 52: Case Study #7
Correct fluid level verified
Vehicle shudder reproduced during test drive
Snapshot reveals engine, turbine and output speed change rapidly at point shudder occurs

## Slide 53: Case Study #7
Engine, turbine and output speeds are 1339 rpm before shudder
  Increase to 1450 rpm then decrease to 1232 rpm then increase to 1441 rpm
  Continue to accelerate/decelerate until all speeds return to same rpm
All three speed traces change identically at a physically possible level and frequency
  Eliminates electrical noise as cause
Electrical noise further eliminated on speed sensor circuits due to shudder occurring when transmission is not executing a shift

## Slide 54: Case Study #7
All three speed signals changing in a manner identical in shape with one another indicates an external force creating accelerations/decelerations on the output or turbine shafts
Vehicle driveline can be eliminated
  Based on operating conditions that must be present for shudder to occur
  Excessive universal joint torsional/inertial accelerations are not temperature dependent
    Would not occur only once during vehicle operation until ignition switch is cycled
  Eliminates forces entering transmission at output shaft

## Slide 55: Case Study #7
Turbine shaft remains only entry point where force can be imparted
  Coming from engine output
Vehicle sent to local engine distributor for investigation
  Engine fuel pump was determined to be cause of vehicle shudder

## Slide 56: Case Study #8
Issue
  Customer complaining of harsh 5-4 downshifts, “step-through” shift is really bad
    Vehicle mileage at complaint 2,412 (3,882 Km)
    No DTCs
Transmission
  3000 Series
Vocation
  Bus

## Slide 57: Case Study #8
Correct fluid level verified
Complaint reproduced during test drive
Snapshot reveals all speeds become erratic after 5-4 downshift occurs
  Output speed is not smooth and changes in output speed are “mirrored” (to a lesser degree) by turbine and engine speed traces after shift into 4th

## Slide 58: Case Study #8
Engine problem is not perceived
Driveline inspected
  Found in good condition
Driveline angles measured
  Universal joint accelerations calculated
    Torsional – 1025 rad/sec/sec
    Internal Drive – 309 rad/sec/sec
    Inertial Coast – 3799 rad/sec/sec
Driveline shows incorrect angularity creating high torsional accelerations

## Slide 59: Case Study #8
Incorrect driveline angularity creating high torsional accelerations and inertials
  Torsional accelerations should be < 500 rad/sec/sec
  Inertials should be < 1200 rad/sec/sec

## Slide 60: Case Study #9
Issue
  Customer complaining of delayed 2-1 downshift since beginning of truck operation
    Vehicle mileage at complaint 18,722 (30,130 Km)
    No DTCs
Transmission
  3500 Series
Vocation
  Refuse

## Slide 61: Case Study #9
Correct fluid level verified
Complaint reproduced during test drive
Technician replaced TCM and PCS3 solenoid prior to requesting assistance
Allison DOC® connected to transmission
  PCS3 solenoid commanded full on for brief time to initiate application of C5 clutch
    Solenoid modulated after full on command to smoothly apply C5 clutch
  Turbine speed does not increase during this test

## Slide 62: Case Study #9
TCM senses turbine speed is not decreasing and commands PCS3 solenoid on full in an attempt to apply C5 clutch
  Turbine speed decreases indicating C5 clutch is applied
100% throttle 1-2 shift is good, driver only complains of delayed 2-1 shift at closed throttle
  2-1 adaptive shift is reset with DOC
    Delay is eliminated for a few days then returns

## Slide 63: Case Study #9
Rules out potential wiring/connector issue
  100% throttle 1-2 shift would also be affected if:
    PCS3 solenoid circuit resistance is above specification
    Copper wire strands are insufficient to conduct enough current
C5 clutch test performed with Allison DOC®
  Pressure shown within specification
  Test drive performed to reproduce complaint
    C5 clutch pressure falls below specification during 2-1 closed throttle shift
    C5 clutch requires most volume to actuate piston
Engine idle speed is showing lower than typical
  600-700 rpm
    Falls within Tech Data minimum specification
  Customer has identical trucks operating at same idle speed with no issues

## Slide 64: Case Study #9
Transmission is equipped with a PTO
  PTO main pressure supply line disconnected from transmission main pressure tap
Test drive repeated
  2-1 shift delay is eliminated
PTOs must utilize an orifice in either the supply line or the orifice must be in the PTO
  In this case, the PTO utilizes an orifice in the PTO
  PTO is replaced
  2-1 downshift issue is resolved

## Slide 65: Static Data
Specific information stored in the TCM that can be extracted and reviewed
  Aids in troubleshooting process
  Functionality began with Allison 4th Generation Controls
Data extracted includes:
  Clutch applies
  Sump fluid temperature
  Retarder fluid temperature
Extracted values are total quantity of clutch applies and time at temperature
  Data is specific to each individual TCM

## Slide 66: Static Data
Data contained in TCM memory is from beginning of vehicle operation
  If TCM is original to the vehicle
  Replacement TCMs only contain data going back to installation of new TCM
Recalibrating TCM does not erase static data from memory
  Research warranty database to determine if TCM is a replacement TCM

## Slide 67: Static Data
Collecting Static Data
  Open Allison DOC®
    Be sure translator device is connected to transmission
    Ignition on with engine on or off
  Select Read Static Data option under Action Request menu

## Slide 68: Static Data
Confirm communication adapter setup
  Extraction process begins after clicking OK

## Slide 69: Static Data
Provide detail information and click OK
  Confirmation window displayed upon successful operation
    Saved file location displayed

## Slide 70: Static Data
View Static Data file information
  Use Allison ACE program
    Contained within Allison Datalog program
Access ACE
  Click My Computer and local C: drive
    Or location where Gen4 or Gen5 programs are installed
  Click gen4 or gen5 folder

## Slide 71: Static Data
Access ACE (cont’d)
  Double-click winace32 icon

## Slide 72: Static Data
Open S2 file
  Click “from disk” icon
  Locate S2 file and select Open

## Slide 73: Static Data
Click “Goto” button in opened ACE file
Select PO Table from drop down menu

## Slide 74: Static Data
Selected desired table
  Oil_Life_Temps_Times selected for this example

## Slide 75: Static Data
Selected table is displayed
  Some units may need to be converted if extracted data is from MY09 or Gen4 calibration

## Slide 76: Static Data
Table data can be exported to Excel
  Select Excel button
  Click “ToExcel” button
  Excel opens and imports data from ACE table

## Slide 77: Static Data
Extracted data example
  Fluid temperature data chart
Time in Ace file given in seconds.
Prior to MY09 Prognostics (CIN beginning with 4A) time is in actual seconds.
Beginning with 4A calibrations, seconds must be multiplied by 0.025 to calculate actual time.
The value of 0.025 will convert seconds to hours.
Beginning with Gen6, time is in actual seconds.

## Slide 78: Data Bus Viewer
Allows all data available on vehicle datalink to be monitored
Does not communicate with any controller
  Including TCM
  Only monitors data as it flows through datalink
Many Input, Output and mandatory functions are available on the J1939 datalink
  Reverse Warning
  Neutral Start

## Slide 79: Data Bus Viewer
Beginning with Gen4, calibrations can be configured to have I/O functions assigned to
  Wires only (analog)
  Databus only (digital)
  Wires and Databus
    Both analog and digital signals are required for proper function operation
  Wires or Databus
    TCM reacts to either signal
    If both are present, TCM generally ignores analog signal
And means both signals must be received by TCM for proper function operation
Or means only one signal must be received by TCM for proper function operation

## Slide 80: Data Bus Viewer
Example
  Input function “Auxiliary Function Range Inhibit Standard” (AFRI)
    Neutral to range shifts are inhibited when AFRI function is active
      AFRI is an inverted function
  Information for this example shown via DOC in following progression
    Pre MY09 software
    MY09 software
      CIN beginning with 4A
    Gen5 software

## Slide 81: Data Bus Viewer
Example (cont’d)
  Determine if I/O function is available for use on J1039 on pre-MY09 software
    Input CIN in to Allison PCCS software
    Generate Calibration Summary report
      Report will indicate Yes or No if an I/O is programmed to be available on J1939 datalink
  If a function is programmed in calibration to be available on J1939 it cannot be disabled with Allison DOC®

## Slide 82: Data Bus Viewer
Example (cont’d)
  Wire State and Function State relationship
    If I/O is not inverted
      Function is OFF when circuit is OPEN
    If I/O is inverted
      Function is ON when circuit is OPEN
    OPEN circuit = function ON
    CLOSED circuit = function OFF
  In Allison DOC®:
    Wire State (pre-MY09) and Signal State (MY09) shows OFF for an inverted function
      Indicates a CLOSED circuit exists

## Slide 83: Data Bus Viewer
Example (cont’d)
  AFRI – Wire Input

## Slide 84: Data Bus Viewer
Example (cont’d)
  AFRI – Analog Wire and J1939

## Slide 85: Data Bus Viewer
Example (cont’d)
  AFRI – Analog Wire or J1939

## Slide 86: Data Bus Viewer
Example (cont’d)
  AFRI –J1939 Input (wire disabled)

## Slide 87: Data Bus Viewer
Example (cont’d)
  AFRI –J1939 Input (wire disabled) (cont’d)

## Slide 88: Data Bus Viewer
Example (cont’d)
  AFRI –J1939 Input ONLY

## Slide 89: Data Bus Viewer
Example (cont’d)
  AFRI –J1939 Input ONLY (cont’d)

## Slide 90: Data Bus Viewer
Example (cont’d)
  MY09 and later DOC I/O grid enhancement example
    AFRI – Wire disabled

## Slide 91: Data Bus Viewer
Example (cont’d)
  MY09 and later DOC I/O grid enhancement example (cont’d)
    AFRI – Wire enabled

## Slide 92: Data Bus Viewer
Example (cont’d)
  MY09 and later DOC I/O grid enhancement example (cont’d)
    AFRI – Gen5 grid example

## Slide 93: Data Bus Viewer
Accessing Data Bus Viewer
  Select Connect
  Select transmission series
    Click Data Bus Viewer button

## Slide 94: Data Bus Viewer
Accessing Data Bus Viewer (cont’d)
  Select communications adapter device being used
  Select J1939 protocol

## Slide 95: Data Bus Viewer
Accessing Data Bus Viewer (cont’d)
  Leave Save Data Continuously option unchecked
    Only saves last two minutes of databus data

## Slide 96: Data Bus Viewer
Accessing Data Bus Viewer (cont’d)
  Select Save when data collection is complete
    Name file

## Slide 97: Data Bus Viewer
Accessing Data Bus Viewer (cont’d)
  Playback file
    Select Playback Data Bus Viewer Files from File menu

## Slide 98: Data Bus Viewer
Accessing Data Bus Viewer (cont’d)
  Playback file (cont’d)
    Click Open Data Bus Session
    Choose file and click Open button

## Slide 99: Data Bus Viewer
Accessing Data Bus Viewer (cont’d)
  Playback file (cont’d)
    File is displayed

## Slide 100: Data Bus Viewer
Accessing Data Bus Viewer (cont’d)
  Playback file (cont’d)
    Expand Source Address (SA) to view related data

## Slide 101: Datalink Tech Data
Accessing Datalink Tech Data
  Allison Extranet
    Engineering section

## Slide 102: Datalink Tech Data
Accessing Datalink Tech Data
  Click Datalink Communications link

## Slide 103: Datalink Tech Data
Accessing Datalink Tech Data
  Select Control System
  Click “List of all documents in this section”
  Select software level

## Slide 104: Datalink Tech Data
J1939-based vehicle function Overview
  Clicking on function shows details including
    All J1939-based functions
    Allison family availability
    Equivalent wire function

## Slide 105: Datalink Tech Data
J1939 Function Information
  Availability vs. Software Level
  J139 Parameter & SA Requirements
  Driver Interface Requirements
    Including bulb checks, labeling, etc.
  Other Requirements/Restrictions
  Normal Operation
    Data use when things are working correctly
  Failure Modes & Responses
    Controls response to bad or lost data
    How other device(s) should react to problems
  Installation Checklists
    Allows vehicle OEM or Allison personnel to verify correct implementation of the function

## Slide 106: Datalink Tech Data

## Slide 107: Datalink Tech Data
J1939 Function Information – Example 1
  Issue
    Problem with J1939 communication link
  Background
    Engine controller presents DTC indicating no communication with transmission TCM
    Allison DOC® cannot establish communication with transmission

## Slide 108: Datalink Tech Data
J1939 Function Information – Example 1 (cont’d)
  Process
    Connect Data Bus Viewer to vehicle from DOC file menu
    Read J1939 messages and look for detected messaged
      Only messages detected are from engine ECM and shift selector
      No messages detected from transmission TCM or any other controller

## Slide 109: Datalink Tech Data
J1939 Function Information – Example 1 (cont’d)
  Cause
    Backbone is open/shorted after shift selector

## Slide 110: Datalink Tech Data
J1939 Function Information – Example 2
  Issue
    Transmission will not attain any forward or reverse range
  Background
    Calibration supports Auxiliary Function Range Inhibit Standard
    Calibration is set to use analog and J1939 signals
  Vehicle
    School bus

## Slide 111: Datalink Tech Data
J1939 Function Information – Example 2 (cont’d)
  Process
    Connect DOC and open Data Monitor
    Transmission currently in Neutral

## Slide 112: Datalink Tech Data
J1939 Function Information – Example 2 (cont’d)
  Process (cont’d)
    Close door
      Connected to wire 101
    Apply brakes
    Function does not deactivate
      Inhibit is still present

## Slide 113: Datalink Tech Data
J1939 Function Information – Example 2 (cont’d)
  Process (cont’d)

## Slide 114: Datalink Tech Data
J1939 Function Information – Example 2 (cont’d)
  Process (cont’d)
    Use Data Bus Viewer to look for J1939 parameters associated with AFRI
      CVVS – Brake Switch
        broadcasted from SA 00, 33, 17 or 49
      EBC1 – EBS Brake Switch
        broadcasted from SA 11

## Slide 115: Datalink Tech Data
J1939 Function Information – Example 2 (cont’d)
  Process
    Close door (wire 101) and apply brakes
      CC/VS – SA(00) – Brake Switch does not indicate brakes have been depressed
  Cause
    TCM is waiting for J1939 service brake input signal to remove inhibit
      Message not being sent by CC/VS controller
      TCM maintains inhibit

## Slide 116: Datalink Tech Data
J1939 Function Information – Example 2 (cont’d)
  Other potential scenarios
    Data Bus Viewer indicates CC/VS and EBC1 are not available
      Calibration is setup to receive service brake status over J1939
    Data Bus Viewer indicates CC/VS is reflecting correct service brake status
      EBC1 is present and is not reflecting service brake state
      EBC1 has higher hierarchy than CCVS
        TCM does not eliminate inhibit