## Slide 1: Introduction
Vibration and noise can be some of the most difficult conditions to troubleshoot
  Very subjective
  Difficult to describe accurately
Frequently, transmission is incorrectly blamed for:
  Driveline induced failures
  Vibration and noise

## Slide 2: Vibration
All mechanical systems will vibrate
Vibration is cyclic displacement versus time
  Displacement measured in Amplitude (A)
  Frequency measured in cycles/second (Hz)
Every system has a Natural Frequency
  Determined by mass/elastic characteristics of system

## Slide 3: Vibration
Examples of natural frequency:
System | Mass/Elastic Characteristics
Pendulum | Length of string
Guitar string | Length, tension, diameter of wire, etc.
Tuning fork | Shape, length of legs, material, etc.

## Slide 4: Resonance
External force causes resonance when:
  Force is cyclical
  Frequency of force is approximate/equal to the natural frequency of the mass/elastic system
Condition of resonance
  Small external force creates high system amplitudes
    Can cause system failure

## Slide 5: Resonance
Simple example – Child’s swing
  Natural frequency is determined by length of chains
  External force is person pushing child
  If person pushes child at natural frequency of the system:
    Only a small force is required
    Child goes higher and higher

## Slide 6: Torsional Vibration
Variation in angular velocity about the average angular velocity of a rotating shaft in a dynamic system
Another definition
  The periodic motion of a shaft in which the shaft is twisted about it axis
    First in one direction, then the other
  Periodic motion
    Motion that recurs repeatedly
    Period of time required for each re-occurrence remains the same

## Slide 7: Torsional Vibration
Engine, transmission, driveline, axle and wheels form a dynamic mass system
  When transmission lockup clutch is applied
  Engine is primary forcing function exciting this mass/elastic system (powertrain)
Engine torque is not constant during crankshaft rotation
  Torque varies as a function of crankshaft position for each cylinder
Engine firing pulses (order) are a periodic forcing function

## Slide 8: Torsional Vibration
Powertrain system response to engine excited torsional vibration presents a range of consequences
  Component failure
  Unacceptable noise and vibration

## Slide 9: Torsional Vibration
Transmission shifts alter vehicle mass/elastic system
  Engine speed change due to shifts changes engine firing frequency
  In converter mode, transmission does not transmit engine torsionals to rest of powertrain
  With lockup applied, lockup clutch can transmit engine torsionals
  Interior noise and/or vibration may be associated with transmission shifts
    Vehicle system response to engine firing pulses

## Slide 10: Torsional Vibration
Torsional vibration can also be excited by driveline universal joints or driven equipment
Drivelines that do not meet Allison requirements can excite torsional vibration
  Including inter-axle drive shafts
Instantaneous torque absorption of driven equipment (forcing function) can excite torsional vibration
  Can produce dynamic torque exceeding limits for shaft life
  Accumulates cycles rapidly
    1 million cycles in 10 to 20 hours is not uncommon

## Slide 11: Torsional Vibration
Excitation Orders
  Frequency is determined by
    Order X RPM / 60 = Cycles/Second (Hz)
  Third Order excitation
    An even fire, 4 stroke six cylinder engine has an ignition event every 120 degrees of crankshaft rotation
    In 360 degrees of crankshaft revolution, three ignition events occur
      Produces a third order excitation
    Considered periodic motion
      Point of ignition is relatively the same for each piston at a given speed

## Slide 12: Torsional Vibration
Excitation Orders (cont’d)
  Third Order excitation (cont’d)
    Change in time or rate can be measured in frequency
    Example:
      Even-fire 6-cylinder engine operating at 800 rpm vs. 1500 rpm
      With three ignition events per revolution, frequency of periodic motion is
        3 x 800 / 60 = 40 Hz
        3 x 1500 / 60 = 75 Hz

## Slide 13: Torsional Vibration
Excitation Orders (cont’d)
  Second Order excitation
    Driveline periodic forcing function for Carden style universal joints is always second order
Classifying vibration
  Explained in Driveline Troubleshooting Manual
  Explained in Driveline section of this training program
    Reference the Vibration Flow Chart

## Slide 14
Case Study #1
Issue
  Fractured flex plates (first failure)
  Fractured torque converter (second failure)
    Vehicle mileage at first failure 152,215 (244,966 Km)
    Vehicle mileage at second failure 168,810 (271,674 Km)
Transmission
  4000 Series
Vocation
  Heavy Hauler

## Slide 15
Case Study #1
Inspections revealed
  Transmission properly installed to engine flywheel housing
  No fractures in transmission torque converter housing or engine flywheel housing
  Crankshaft bolts tight
  Flexplate assembly correct for engine
    Four flexplates present
  Crankshaft endplay measured within engine manufacturer specifications
  Excessive radial movement not found on rear crankshaft flange when pushed up/down
  All engine adaptation components within specification
    Per SIL 60-TR-81

## Slide 16
Case Study #1
Inspections revealed (cont’d)
  No apparent engine problem relating to misfire or excessive vibration
  Torque converter pump tangs are fractured in tang root area
    Tangs are not bent, battered or worn
  Charging pump bushing journal surface not worn on one side
  Ruled out
    Improper transmission fluid maintenance
    Out-of-flat transmission front support

## Slide 17
Case Study #1
Inspections revealed (cont’d)
  Truck equipped with engine driven hydraulic pump
    Pump driven via driveshaft from front of crankshaft
    Driveshaft equipped with Carden style U-joints
  Possibility of physical issue with flexplates and converter pump tangs are extremely low
    Pump tang fracture not common secondary damage from flexplate failure

## Slide 18
Case Study
Component damage found:
Fractured flex plate
Fractured flex plates

## Slide 19
Case Study
Component damage found:
Pump tangs
Crankshaft flange
Charging pump bushing journal

## Slide 20
Case Study #1
Situation is unique
  Troubleshoot further to determine
    Is something unique on vehicle?
    Unique operation or environment?
Crankshaft driven pump is not common
We know torsional vibration can also be excited by driveline U-joints or driven equipment
  Inter-axle driveshafts not within Allison requirements can excite torsional vibration
  Instantaneous torque absorption of driven equipment can excite torsional vibration
    Can produce dynamic torque exceeding limits for shaft life and accumulates cycles rapidly

## Slide 21
Case Study
Images of installed pump

## Slide 22
Case Study #1
Angularity of pump driveshaft universal joints measured as follows:
  Torsional is 31 rad/sec/sec
  Inertial Drive is 1459 rad/sec/sec
  Inertial Coast is 1429 rad/sec/sec
Vehicle driveline maximum limits to not apply to this type of driveline
  Subject maximum limits for “Input” style drivelines

## Slide 23
Case Study #1
“Input” style driveline maximum limits (based on a 4 degree maximum angle at speeds below 3000 rpm)
  Torsional is 100 rad/sec/sec
  Inertial Drive is 500 rad/sec/sec
  Inertial Coast is 500 rad/sec/sec
Lower acceleration limits due to damaging effects of Secondary Couple
Per Tech Data:
  Driveline is Intersecting Shafts design
  Intersecting axes designs are not allowed

## Slide 24
Case Study #1
Truck does not have a remote mounted transmission with an input driveline
General guideline used for determining maximum continuous U-joint operating angle for intersecting axes:
  Joint angles must be maintained smaller due to less favorable summation of forces which produce the couples
    Maximum continuous running joint angle should be less than L/10
      “L” is shaft length in inches

## Slide 25
Case Study #1
Shaft length is 10 inches
  10 / 10 = 1 degree maximum operating angle
    For both U-joints
Per driveline calculation, “effective” operating angle is:
  Torsional- 6.46 degrees
  Inertial Drive- 9.62 degrees
  Inertial Coast- 7.83 degrees
If amplitude/frequency of U-joints is great enough it can excite torsional vibration
  Can couple with natural frequency of other components in mass/elastic system
    Engine/torque converter/transmission rotation components/drive shafts/axles/wheels

## Slide 26
Case Study #1
We know:
  An External Force causes resonance when force is cyclical in frequency
  Frequency of force is approximate/equal to natural frequency of the mass/elastic system
  Condition of resonance is a small external force creating high system amplitudes which can cause system failure
  If the amplitude of periodic motion of a shaft in which the shaft is twisted about its axis first in one direction, then the other:
    Exceeding design limits of shaft will cause shaft failure

## Slide 27
Case Study #1
Conclusion
  Flexplates are like a shaft between the engine crankshaft and torque converter assembly
  If the variation of angular velocity “twist” is too great, fracture will occur
  Recommended customer adjust universal joints to a maximum of 1 degree

## Slide 28
Case Study #2
Issue
  Fractured P2 carrier
    Vehicle mileage between 50,000 – 80,000 (80,467 – 128,748 Km)
Transmission
  2000 Series
Vocation
  Pickup/Delivery and school bus

## Slide 29
Case Study #2
Background
  Various customers between 2006 and 2008 experience approximately 255 failures of P2 carrier
    One particular large rental truck customer experience 62% of overall failures
  Failed P2 carriers are returned to Allison Indianapolis for inspection and analysis

## Slide 30
Case Study #2
Findings
  Fracture origin is consistently at a lubrication hole
  Fracture mode is torsion
  Material and geometry are within specifications

## Slide 31
Case Study #2
Findings (cont’d)
  Engine power is confirmed within transmission input ratings
  Issue only experience with one OEM
    In each instance same model engine was present

## Slide 32
Case Study #2
Diagnosis
  Truck experiencing multiple P2 carrier failures selected for vehicle torsional measurements

## Slide 33
Case Study #2

## Slide 34
Case Study #2
How much misfire is sufficient to cause a failure?
How low does the cylinder pressure have to be to cause a large enough ½ order amplitude to fail the P2 carrier?

## Slide 35
Case Study #2
Answer is engine and vehicle system dependent
  A single cylinder pressure must go low enough to generate levels of ½ order torsional amplitudes at the output of the engine
    Will cause the damper mode resonance to be established in the vehicle power pack with great enough limits to exceed P2 hub’s fluctuating stress limits
      At a given mean stress level as defined by a Goodman diagram (above left)
    Level of engine excitation required is dependent upon damping within system

## Slide 36
Case Study #2
Engine torque variation for each cylinder of a six cylinder engine for two crankshaft revolutions (720 degrees of rotation):
  ½ order frequency found was due to faulty fuel injector
    Causing one cylinder to not produce power matching other five
Starting on left, engine should have an ignition event every 120 degrees of crankshaft rotation
  Ignition occurs twice, but not third time during 360 degrees of rotation
    Remaining three cylinders have ignition during 2nd 360 degrees of rotation
  Determine order of missing cylinder by dividing revolutions by missing cylinder
    2 revolutions / 1 cylinder = ½ Order

## Slide 37
Case Study #3
Issue
  Fractured flexplates
    Customer experienced numerous failures in fleet between 18 and 22 months of operation
Engine
  Detroit Diesel Series 60
Transmission
  4500 Series
Vocation
  Dump truck/Tipper

## Slide 38
Case Study #3
Inspections revealed
  Transmission properly installed to engine flywheel housing
  No fractures in transmission torque converter housing or engine flywheel housing
  Crankshaft bolts tight
  Flexplate assembly correct for engine
  Crankshaft endplay measured within engine manufacturer specifications
  Excessive radial movement not found on rear crankshaft flange when pushed up/down
  All engine adaptation components within specification
    Per SIL 60-TR-81

## Slide 39
Case Study #3
Inspections revealed (cont’d)
  Set of flexplates were found that had begun to crack but had not failed
    Discovered in one of the fleet trucks
    Flexplates, wearplate and crankshaft hub adapter returned to Allison Indianapolis for inspection

## Slide 40
Case Study #3
Component damage found:

## Slide 41
Case Study #3
Findings
  Four flexplates were labeled as to position in assembly
    Red dye penetrant and white developer present on plates
    Contact patterns between detail parts were closely examined
      Labeling/sequencing of flexplates as received was verified as correct
  All flexplates had cracks originating around crankshaft bolt holes
    Each plate had at least five cracks
    Some plates had more
  Some cracks on each plate propagated tangentially outward from center area for a short distance

## Slide 42
Case Study #3
Findings (cont’d)
  Front-most plate (located against crankshaft hub adapter) was only cracked on transmission side
    No cracks present on engine side
  Remaining three rear plates had cracks extending through thickness of plates
  Cracks at crankshaft bolts originated in area between stress cone
    From the bolted clamp load and hub adapter/wear plate OD
  Scanning Electron Microscope (SEM) showed significant rubbing occurred on fracture surfaces
    Destroyed most fractographic features
    Minute areas at edges were found exhibiting fatigue striations due to bending fatigue

## Slide 43
Case Study #3
Findings (cont’d)
  No mechanical or material defects were noted during SEM examination that would have aggravated failure
  Fretting corrosion of flexplates was of appreciable depth
    In several instances
    Degree of fretting between interfaces varied
      Worse at outer interfaces of assembly
        Especially at wear plate/flexplate 1 interface
        Somewhat better at crank hub/flexplate 4 interface
        Much less at inner interfaces

## Slide 44
Case Study #3

## Slide 45
Case Study #3

## Slide 46
Case Study #3

## Slide 47
Case Study #3

## Slide 48
Case Study #3
Findings (cont’d)
  Wearplate and crankshaft hub adapter all meet material and hardness requirements
  Failures of flexplates initiated in the annular region between the stress cone of the bolt clap and the OD of the crankshaft hub/wearplate
    The “between” region referred to later
  This zone, being held between crankshaft hub adapter and wear plate provides sufficient restraint/support
    A purely bending fatigue failure should have started at wear plate/crankshaft hub OD
      This pivot location would be highest bending stress location

## Slide 49
Case Study #3
Findings (cont’d)
  Fatigue originating elsewhere indicates some other failure mechanism was taking place to cause failure
  All joints in assembly exhibit fretting corrosion
    Fretting generally occurs between tight-fitting surfaces intended to be fixed in related on each other but undergo minute alternating relative motion (slip)
      Usually due to vibration
  Fretting is a repetitive process
    Oxide surface film typically present on metallic surfaces is disrupted
      Exposes fresh metal surface that quickly oxidizes due to presence of air/oxygen

## Slide 50
Case Study #3
Findings (cont’d)
  Vibratory input repeats cycle
    Material is lost form part surfaces as accumulation of oxides
    Reddish brown Fe2O3 or black Fe3O4 oxides typically accumulate in iron/steel
      Provides telltale fretting signature
  Apparent (from figure 1)
    Stress cone (clamp zone under bolt) head is below wear plate OD
    Portion of flexplate in “between” regions are more susceptible to torque loads exceeding design of clamp load
    Plates are held in intimate contact
      Being sandwiched between adapter hub and wearplate
      Due to reduced clamp load of being in stress cone plates are able to move under applied strain
        Exceeding design limits

## Slide 51
Case Study #3
Conclusions
  Oxide residue created by fretting corrosion occupies more volume that initial iron
    As fretting progressed
      Corrosion residue accumulated within bolted joint
      Packed joint with debris
      Oxidized debris can be harder than steel surfaces in contact
        Especially Fe2O3
      Abrasive wear of mating surfaces with further micro movement of joint is inevitable

## Slide 52
Case Study #3
Figures 12 & 13 – Optical photograph of flexplate 4 showing the transmission-facing and engine-facing surfaces respectively at same magnification (original magnification 5x)

## Slide 53
Case Study #3
Figure 14 – Optical photograph of engine-facing wear plate contact surface (original magnification 5x)

## Slide 54
Case Study #3
Figure 15 – Optical photograph of transmission –facing crankshaft hub contact surface (original magnification 5x)

## Slide 55
Case Study #3
Conclusions (cont’d)
  Missing/thinned flexplate material created a mechanical stress riser
    Initiated bending fatigue failure within annular zone of bolted joint
  Discovered from customer:
    Engines in all trucks would intermittently misfire
      Creating violent vibration throughout truck
    Identical engine in trucks equipped with manual transmissions were experiencing same issue
      Fracturing clutch damper springs/frames

## Slide 56
Case Study #3
Conclusions (cont’d)
  Final conclusion
    Engine is producing torque loads exceeding design of clamp limit when misfire occurs

## Slide 57: Sound
Defined as any pressure variation the human ear can detect
  In air, water or other medium
Barometer is the most familiar instrument for measuring air pressure variations
  Pressure variations occurring with changing weather conditions are much too slow for human ear to detect
    Do not meet definition of sound

## Slide 58: Sound
Sound is considered variations in atmospheric pressure occurring at least 20 times per second
  Can be detected by human ear
Number of pressure variations per second is the frequency of sound
  Measured in Hz
  Produces distinctive tone
    Rumble of thunder has low frequency
    Whistle has high frequency

## Slide 59: Sound
Normal range of human hearing for healthy young person
  20Hz to 20,000 Hz (20 kHz)
Range of lowest to highest piano note
  27.5 Hz to 4186 Hz
Pressure variations travel through any elastic medium (such as air)
  From source of sound to listener’s ear

## Slide 60: Sound

## Slide 61: Sound
Speed of sound
  5 seconds per mile (3 seconds per kilometer)
  770 mph (1238 km/h)
  For acoustic and sound measurements
    Speed expressed at 344 meters per second at room temperature
A sound with only one frequency is called a pure tone
  Pure tones seldom encountered
  Most sounds made of different frequencies
  Even single note on piano has a complex waveform
Most individual noises consist of a wide mixture of frequencies
  Broad band noise

## Slide 62: Sound
Decibel (dB)
  Used to measure size or amplitude of pressure fluctuations
    0 dB corresponds to threshold of hearing
      10 dB increase required for a sound to subjectively appear to be twice as loud
    3 dB is smallest change humans can hear
Subjective (perceived) loudness of a sound is determined several complex factors
  Human ear not equally sensitive to all frequencies
    Most sensitive to sounds between 2000Hz and 5000 Hz
    Less sensitive to higher and lower frequencies

## Slide 63: Sound
Impulse sounds present other problems in loudness evaluation
  Short duration sound (less than one second)
    Ear is less sensitive to loudness perception due to short duration
Sound is typically measured using an “A’’ weighting
  Designated with dB(A) units
Follow sound meter manufacturer’s direction for
  Distance
  Orientation
  Outside environmental conditions
  Not following directions leads to inaccurate measurements

## Slide 64: Sound
Classifying sound
  Difficult for customers and technicians alike
  Similar to classifying vibration
    Has noise always been present?
    Under what operational conditions does the noise occur?
    Under what conditions is the noise loudest?
    Under what conditions is the noise most quiet?
    Is the noise a constant sound?
    Does the noise oscillate/vary?

## Slide 65: Sound
Classifying sound (cont’d)
  Similar to classifying vibration (cont’d)
    How would you describe the noise?
      Rattle
      Squeal
      High frequency buzz
      Grinding
      Whine
      Clunk
      Rumble
      Squawk
      Groan